## Slide 1: Gain Simulations

## Slide 2: Recap and Goal
We concluded from previous work and calculations – need 2000 injector cycles with 16 fills for a laser of 12.5 kHz to obtain the 140 points separated by 5 ms – our goal.
In this work we consider the effect of the long term gain for these 2000 cycles considering both, the gains of the PMT’s of the laser monitoring system and the SiPM’s.
To begin with we consider the SiPM’s to have an exponential gain given by - G(t) = 1+ε exp(‐t/τ), which is measured by laser pulses fired every 5 ms.
We simulate an exponential decay for 2000 events measured at an interval of 5 ms by laser pulses (the details explained shortly)
PMT gain is just a linear step function that remains constant for a firing time (of 5 ms).

## Slide 3: PMT - Gain
Assume 2% gain change in PMT’s for our measurement period of about 1 hr (2000 cyles)
We need 2000 cycles – in essence this is just a step function following : Pi = 1+0.00001 x i, here i the cycle number

## Slide 4: SiPM – Gain measured with a Laser
Fixing the time (every 5 ms) a Gaussian distribution is simulated for 2000 events with mean as the value of G(t) and a sigma of 2% of the mean. The example of G(140) – last bin is shown here. A histogram of all these points is our simulated normal gain (top panel of slide # 5).
Next we measure this gain for each cycle which is effected by P(t). A histogram of G(t) / P(t) modified gain (middle panel of slide # 5). Finally modified gain in units of normal gain is plotted and used (bottom panel of slide # 5).

## Slide 5
SiPM Exp Gain – epsilon = 0.001
We started with an exponential function, but will study other perturbations (linear, cos etc.)

## Slide 6: SiPM Exp Gain – epsilon = 0.005

## Slide 7: Compare different gains
Just a check I used two values of e in G(t). Final gains as shown below (previous 2 slide have the other histograms). Shape is almost the same. Used cubic spline (TSpline3) to interpolate the normalized modified gain.

## Slide 8: SiPM Exp Gain for 2000 and 5000 pts

## Slide 9: SiPM – Gain different epsilons
We compare the nature of the modified gain functions finally used R(t) for gain fluctuations effecting the frequency – overlaid all below

## Slide 10: Stable wiggle plot
Stable wiggle plot showed no difference (obviously should not). Just a sanity check.

## Slide 11
Start time scan for the stable case

## Slide 12
Start time scan for the stable case – R and chi2
c2/NDF

## Slide 13: SiPM – Exp Gain – one cycle
Wiggle plots using normalized modified gain for two values of e.

## Slide 14
Start time scan for the exp case e=0.001

## Slide 15
Start time scan for the exp case e=0.001

## Slide 16: SiPM Linear Gain – epsilon = 0.001

## Slide 17: SiPM – Linear Gain

## Slide 18
Start time scan for the Linear case e=0.001

## Slide 19
Start time scan for the linear case e=0.001

## Slide 20: SiPM Phase Gain – epsilon = 0.001

## Slide 21: SiPM – Phase Gain

## Slide 22
Start time scan for the Phase case e=0.001

## Slide 23
Start time scan for the Phase case e=0.001

## Slide 24: Questions?
In fill means data taking along with the beam. Out of fill is when we do not have beam or run b/w fills. As I understand this would be ok for calibrating but w/o the beam how can we study the effect of gain on our delta_w – not relevant – Answered…
Effect of the stability /instability of AmNaI source on laser PMT’s?
Should we / can we do an offline study of the PMT and Am source with their effects??